## Slide 1
Equivalent Electrical circuits for Oscillators
Lecture-2

## Slide 2: Mechanical Oscillators
Equation of motion
(undamped case):
m(d2x/dt2) + sx = 0
Solution: x(t) = A cos(ω0t +)
Natural Frequency: (ω0)2  (s/m)
s

## Slide 3: LC Circuit Oscillators
Consider a simple LC (electrical) circuit:
(L = inductor, C = capacitor)
Equation of motion for charge q
(no damping or resistance R):
L(d2q/dt2) + (q/C) = 0 (1)
Kirchhoff’s loop rule  L(dI/dt) + (1/C)∫Idt = 0 (2)
Solution to (1) or (2): q(t) = q0 cos(ω0t +  )
Natural Frequency: (ω0)2  1/(LC)

## Slide 4
A comparison of the equations of motion of mechanical & electrical oscillators gives analogies:
x  q, m  L, s  C-1, (dx/dt)  I
Consider (let  = 0 for simplicity): q(t) = q0cos(ω0t)
 [q(t)]2 = q02 cos2(ω0t) and I(t) = (dq/dt) = -ω0q0sin(ω0t)
 [I(t)]2 = [ω0q0]2sin2(ω0t) = [q02/(LC)]sin2(ω0t)
So: (½)L[I(t)]2 + (½)[q(t)]2/C = (½)[q02/C] (1)
With the above analogies, (1) is mathematically analogous to the total energy for the mechanical oscillator
(½)m[v(t)]2 + (½)s[x(t)]2 = (½)sA2 = Em (2)
From circuit theory, total energy for an LC electrical circuit is Ee  (½)[q02/C]  (1) is also analogous physically to (2)

## Slide 5
Physics: The total Energy of an LC circuit
 (½)L[I(t)]2 + (½)[q(t)]2/C = (½)[q02/C] = Ee = const.!
Physical Interpretations:
  (½)LI2  Energy stored in the inductor
   Analogous to kinetic energy for the mechanical oscillator
  (½)C-1q2  Energy stored in the capacitor
   Analogous to potential energy for mechanical oscillator
  (½)[q02/C] = Ee  Total energy in the circuit  Analogous to the total mechanical energy E for the SHO Also, Ee = constant!  The total energy of an LC circuit is conserved. The system is conservative only if there is no resistance R. As we’ll see, in electrical oscillators, R plays the role of the damping constant. Rm for mechanical oscillators.

## Slide 6: Example 1
Consider a vertical mass-spring system:
~ Similar to a free oscillator, but there
is the additional constant downward
force of the weight F = mg. At
equilibrium, the weight stretches the
spring a distance h = (mg/k)
 There is a new equilibrium position at x = h
 The eqtn of motion is the same as before with
x  x - h . So, it is: m(d2x/dt2) +s(x-h) = 0
with initial conditions x(0) = h +A, u(0) = 0
 Solution: x(t) = h + A cos(ω0t)
s

## Slide 7
Analogous electrical oscillator system
to the vertical mechanical oscillator? 
LC circuit with a battery 
(a constant EMF source ε)!
Equation of Motion?
Kirchhoff’s loop rule gives:
L(dI/dt) + (1/C)∫I dt = ε = [q1/C]
q1  Charge that must be applied to C to produce voltage ε
With I = (dq/dt) this becomes: L(d2q/dt2) + [q/C] = [q1/C] (1)
(1) is mathematically identical to the mass-spring system with a constant external force (gravity). For initial conditions:
q(0) = q0, I(0) = 0, solution is: q(t) = q1 + (q0 - q1) cos(ω0t)
This circuit is an exact electrical analogue to the vertical spring-mass system in a gravitational field.
s

## Slide 8: LRC Circuit
Mechanical
oscillator with damping:
Equation of motion:
m(d2x/dt2) + Rm(dx/dt) + sx = 0
We’ve seen that the general solution is:
x(t) = e-βt[A1 eαt + A2 e-αt]
where α  [β2 - ω02]½
  A1 , A2 are determined by initial conditions: (x(0), v(0)).
ω02  (s/m), β  [Rm/(2m)]
s
Rm

## Slide 9
An LRC circuit is an electrical
oscillator with damping.
Equation of Motion: Kirchhoff’s
loop rule: L(dI/dt)+RI + (1/C)∫I dt = 0 (1)
In terms of charge, I = (dq/dt), (1) becomes:
L(d2q/dt2) +R(dq/dt) + (q/C) = 0 (2)
(2) is identical mathematically to the damped oscillator equation of motion with x  q, m  L, Rm  R, s (1/C)
 General Solution is clearly q(t) = e-βt[A1 eαt + A2 e-αt]
with α  [β2 - ω02]½ ω02  (LC)-1, β  [R/(2L)]
Analogous electrical oscillator system to the damped mechanical oscillator?

## Slide 10: Summary of Electrical-Mechanical Analogies
From the last row, clearly, the mechanical oscillator-electrical oscillator analogy also carries over to the driven mechanical oscillator  driven circuit.
s

## Slide 11: Mechanical Analogies to Series & Parallel Circuits
  The mechanical oscillator with spring constant s is analogous to the inverse capacitance (1/C) = C-1 in an electrical oscillator.
  Inversely, the mechanical compliance  (1/s) = s-1 is analogous to the capacitance C
Consider a circuit with 2 capacitors
C1, C2 in parallel 
  From circuit theory, the
  effective capacitance is
  Ceff = C1+ C2

## Slide 12
For 2 capacitors C1, C2 in parallel 
Effective capacitance: Ceff = C1+ C2
Consider 2 springs with constants
s1, s2 in series 
  Effective spring
  constant (effective compliance):
  (1/seff) = (1/s1)+ (1/s2)
Proof: Apply a force F to 2 springs in series:
  Spring 1 will extend a distance x1 = (F/s1) spring 2 will extend a distance x2 = (F/s2). Total extension:
  x = x1+x2= F[(1/s1)+(1/s2)]  (F/seff)
 2 springs in series are analogous to 2 capacitors in parallel!
s1
s2

## Slide 13
The mechanical oscillator with spring constant s is analogous to the inverse capacitance (1/C) = C-1 in an electrical oscillator.
Inversely, the mechanical compliance  (1/s) = s-1 is analogous to the capacitance C
Consider a circuit with
2 capacitors C1, C2 in series 
  From circuit theory, the
  effective capacitance is
  (1/Ceff) = (1/C1) + (1/C2)

## Slide 14
For 2 capacitors C1, C2 in series 
Effective capacitance: (Ceff)-1 = (C1 )-1 + (C2)-1
Consider 2 springs with constants
s1, s2 in parallel 
  Effective spring constant:
  seff = s1+ s2
Proof: Stretch 2 springs in parallel a distance x:
  Spring 1 will experience a force F1 = s1x, spring 2 will experience a force F2 = s2x. Total force:
F = F1+F2= (s1+s2)x  seff x
 2 springs in parallel are analogous to 2 capacitors in series!
s1
s2

## Slide 15
Draw the equivalent electrical circuit for the following mechanical system and find the mechanical impedance with its corresponding unit, where Rm=1.4 kg/s, s1=30 N/m, m=70 kg and F=2cos 314t
S1
F
Rm
m
Draw the equivalent electrical circuit of the Mechanical system given in Fig.1 and drive the expression of mechanical impedance
S1
F
Rm
S2
m